## Slide 1: Introduction To PLC Programming

## Slide 2: Intro to PLC Programming
PLC programming languages is based on the IEC 61131-3
  Ladder diagram (LD), graphical
  Function block diagram (FBD), graphical
  Structured text (ST), textual
  Instruction list (IL), textual
  Sequential function chart (SFC), graphical

## Slide 3: Intro to PLC Programming
Basic Ladder Logic diagrams components
  Rails
    Are the vertical lines that represent power and ground
    Power flow left to right
  Rungs
    Are the horizontal Lines that connects the rails
  Contacts
    Boolean logic
    Used to represent logic state the of an input or coil
    Normally open contact or normally closed contact symbol
  Coil
    Boolean logic
    Used to control logic state the of an output or contact
  Logic Expression
    A combination of contacts and coils to formulate a desired control operation.
  Address Notation
    Address Based
    Variable Based

## Slide 4: Intro to PLC Programming
Basic Ladder Elements
  Rung
  Open Contact
  Close Contact
  Coil
  Set
  Reset

## Slide 5: Intro to PLC Programming
PLC Scan

## Slide 6: Intro to PLC Programming
Program

## Slide 7: Intro to PLC Programming
Basic Data Types
  Boolean (1 bit)
  WORD (16 bits), DWORD (32 bits)
    does not represent a number only an array of bits
    Most PLC allows you to access these bits using the Dot Operator or [].
  INT (16 bits) – represent a signed number 0 – 65535
  UINT (16 bits) – represent a unsigned number - 0 to 65535
  DINT (32 bits) – represent a signed number (-2147483648) – (2147483648)
  UDINT (32 bits) - represent a unsigned number
  REAL (32 bits) – single precision floating point number (IEEE-754 )
  LREAL (64 bits) –double precision floating point number (IEEE-754 )
  Time (64 bits) – define a time variable (HH:MM:SS:MS:US:NS)
  String ( 8 bits * Char) – defines an array of chars

## Slide 8: Intro to PLC Programming
Array
  Collection of data elements of the same data type
Structure
  Allows of a set of variables to be grouped together
Unions
  Data structure that usually contains different data types
  All components have the same offset
  Occupy the same memory space
Enumeration
  An ordered list of all items in a collection

## Slide 9: Intro to PLC Programming
Write a basic Ladder diagram